## Slide 1
Advanced Contents Distribution Trial 2003 in Japan TVA-IDE@Geneva 7.26.2004 M. Kawamori,NTT

## Slide 2: TestBed on TVA technologies
Major Japanese broadcasters, a carrier and venders worked together for Trial of Integrated Services on Broadcasting and Broadband Networks, implementing various TVA specs.
Tested various ways of creating, acquiring, and consuming content/programs in the new environment.

## Slide 3: Participants
Content provided by:
Japan Broadcasting Corporation (NHK)
Nippon Television Network Corporation (NTV)
TV Asahi Corporation
Tokyo Broadcasting system, Inc. (TBS)
TV Tokyo Corporation
Fuji Television Networks
Infrastructure, including network and PDR, provided by
NTT
Mitsubishi Electric
Hitachi

## Slide 4: Implemented TVA technologies
SP003v13 (PartA) metadata
  Use of EPG/ECG together w/ ARIB-SI
  Full support for segmentation
  User Profile implemented
Implementation of Metadata exchange (incl. queries and submit) for bi-directional network using SOAP (SP006)
Metadata protection in bi-directional case implementing SP007
Content-referencing based on SP004 and SP006
Integration of Scheduled, On-demand, and stored content

## Slide 5: Additional Features
Multiple transport of MPEG2-TS: eg. 64QAM, MPEG2-TS over IP, OnDemand, Data-Carousel, etc.
Content in High Def. as well as in SD.
Implementation of ARIB’s data content spec (B24) as well as B38 (TVA)
Content protection using ARIB-CAS, Account Management, as well as MPEG21-REL
Provision of Gateway between B2B metadata (J/Meta) and B2C metadata (TVA)

## Slide 6
Transmission
Receive
Optical Fiber
Content Distribution
Server
IP transmitter
ＩＰ Video stream service
IP unicast
STB
Metadata Server
DB
Right Management Server
DB
・・・・・
・・・・・
・・・・・
ＩＰ Video on demand service
64QAM
Video stream service
IP multicast
HDD
Content
HDD
Trial Overview
WDM Network G.983.3
Continuing the trial in 2002, we achieved this year High Definition TV transmission via both 64QAM Video stream service and IP Video stream service as well as secure storage control and TV Anytime metadata handling by BML (Broadcasting Markup Language).
BML

## Slide 7: Sample Content Scenarios
Major broadcasters participating in the trial created AV content, data programs, metadata for EPG as well as segmentation metadata, all supporting TVA specs.
Various scenarios envisaged in TVA are experimented.

## Slide 8: Japanese Broadcasting Corp.
time
Preference
for
“Language Programs”
No particular preference
“language teaching program” is target at the PDR on left
The language promotion is targeted using user preference
Targeted promotional programs based on user profile and segmentation

## Slide 9: Nippon Television Network Corp.
Segmentation metadata example
You can select your favorable scenes by segmentation metadata.
1. Normal viewing. T team is offensive.
2. Select T player’s homers scene by BML
3. He hit homers in the second box.
4. You watch the selected homers scene.
© Nippon Television
Networks Corporation
© Tomo-Digi
© Nippon Television
Networks Corporation
© Nippon Television
Networks Corporation
© Nippon Television
Networks Corporation
© Tomo-Digi

## Slide 10: Tokyo Broadcasting system, Inc.
Select K player’s camera by BML
K player’s camera
Normal camera
1. Normal viewing
3. Return to the normal viewing
2. Switched to K player’s camera
by segmentation metadata
Multi-scenario viewing using segmentation and user profile metadata
Viewer with preference for a particular player is given specific segments viewed from different angles, showing that player
© Tomo-Digi
©Tokyo Broadcasting
system, Inc.
©Tokyo Broadcasting
system, Inc.
©Tokyo Broadcasting
system, Inc.
©Tokyo Broadcasting
system, Inc.
©Tokyo Broadcasting
system, Inc.
©Tokyo Broadcasting
system, Inc.

## Slide 11: TV Asahi Corp.
1.Normal viewing. K university are top.
2. Select second interval digest viewing
3. Second interval digest viewing. K university pass.
Near-live viewing of digest using segmentation and
metadata transport
The highlight is played-back from storage, showing where the previous first runner was passed
© Tomo-Digi
©ＴＶ Ａｓａｈｉ
©ＴＶ Ａｓａｈｉ
©ＴＶ Ａｓａｈｉ

## Slide 12: TV Tokyo Corp.
Off the air,
Change data broad casting service automatically
Check your interesting scene!
Viewing by the dog ear list
Moving picture
explanation picture
Dog ear list
On the air
More detail
Pay Per View
menu
Making a playlist from segmentation metadata
© Tomo-Digi
© Tomo-Digi
© Tomo-Digi
© Tomo-Digi
© Tomo-Digi
© TV Tokyo
© TV Tokyo
© TV Tokyo
© TV Tokyo
© TV Tokyo
© TV Tokyo

## Slide 13
Thank you 
See you in IBC2004