## Slide 1
Digital Radio Broadcast /
Mobile Telecommunication Integrated Service and Associated Demonstration Experiment
June 13, 2004
ＫＤＤＩ
Technology Development Group
Media Technology Development Section
Toshiyasu Wakayama
to-wakayama@kddi.com
Notes: 【要旨】

## Slide 2
Background
Roles
★ Progress in digital transition of broadcast businesses
⇒ Development of broadcast/telecommunication integrated business
★ Exploitation of new services and business models that take advantage of the integration of digital radio broadcasting and mobile devices through 3 Seg Group (FM Tokyo, Nippon Broadcasting System, JFNC)/KDDI
⇒● Developed a verification experimentation system (mobile device / server)
● Conducted demonstration experiment (March 2004)
●Development of a PDA-style terrestrial digital radio receiver:
・Development of 3 Seg Digital Radio Receiver FM Tokyo / KDDI / Vitec
・Development of device browser/viewer KDDI
●Development of experiment server system KDDI
●Program concept / content production FM Tokyo / 3 Seg Group
●Business model / Service examination FM Tokyo / KDDI / 3 Seg Group
●Demonstration experiment FM Tokyo / KDDI / 3 Seg Group
１．Background: Digital Radio Broadcast / Telecommunication
integrated service development
Notes: ●何回も同じ紹介をしているが、初めての方もいるかもしれないので、復習ということで再度やる。

## Slide 3
Digital Radio
Receiver
3 Seg Groupﾟ
Broadcast station server
KDDI
Broadcast linked
EPG Server
Broadcast linked
Content Server
Telecommunication infrastructure
Development of broadcast
linked server etc.
Development of
a 3 Seg compliant
digital radio
receiver /
interface
Radio program linked
With mobile content
Content linked with
Radio program
PDA
PDA-style terrestrial digital radio receiver
Development of a
Digital Radio Player
(data broadcast browser /
video viewer
Zoomed
Screen
image
(USB
connection)
Broadcast wave
２．Integrated system overview and developed components
・FM Tokyo
・Nippon Broadcasting System
BML
data
video

## Slide 4
３．Exterior view of
PDA-style terrestrial digital radio receiver

## Slide 5
BML Display
Display Video
Display entire screen QVGA
４．Overview of digital radio player loaded on PDA
・Digital radio tuning function ・BML Content display function
・Video Display function (SQVGA/QVGA) ・Mode switch function (standard /video/BML）
・EPG display function ・Telecommunication link control function
Features
Screen display
BML display area
Video
Display area SQVGA
*If video is QVGA, reduced to ¼ size
BML display function
Compliant standard
●ARIB STD-B24
TR-B13

## Slide 6
Tuner
Board
DC/DC
AC Adaptor
Electrical power supply board
MemoryStick
Slot
Helical antenna
Center frequency：VHF190MHz
Antenna length：100mm
Antenna format：1/λ
SDRAM
ＰＤＡ
Main board
1/3seg
OFDM
demodulation
1/3seg
Silicone
tuner
DAC
Earphone
Charger IC
I2C
TS Input
AirCheck
Audio
Data
Video Data
DSM-CC Data
Lithium-ion polymer battery
X 2pcs
Main DSP
Ａｌｐｈａｍｏｓａｉｃ VC01
・OFDM/Tuner control
・Demultiplex processing
・Decode audio （MPEG2-AAC）
・USB Control
・Channel scan
・Audio broadcast record and
playback processing
FLASH
USB 1.1
Audio
-Video
Data
-DSM-CC
Data
５．Configuration diagram for terrestrial digital radio receiver component

## Slide 7
６．PDA-style terrestrial digital radio receiver specification

## Slide 8
1. Program airs favorite song
2. Instruct song file download
on data broadcast screen
3. Authentication/payment
through telecommunication
network
4. File download through broadcast
wave
5. Playback file on device
1. Introduce concert ticket sales
through program
2. Go to ticket sale site from data
broadcast screen through
telecommunication network
3. Purchase, authenticate, payment
File download (music / still image / video etc.)
Ticket sale / radio shopping
Music data
Ticket purchase site
Authentication / payment
Electronic ticket
1. Notification of opinionaire entry on program
2. Fill out opinionaire on data broadcast screen
3. Enter opinionaire through telecommunication network
4. Check status through telecommunication network
Opinionaire entry
・・
・・
ああ
いい
1. View EPG through radio broadcast
2. When more detailed information is desired
3. Acquire detailed program information from EPG screen through telecommunication network
Electronic Program Guide (EPG) transmission
Broadcast EPG
Authentication /
payment
Ticket sale
guide
Acquire detailed EPG info.
・entry
・check status
Broadcast/telecommunication
integrated service use cases

## Slide 9
Implementation overview
★Purpose：Gather comments from trial participants regarding the developed digital radio broadcast and mobile telecommunication integrated service to identify requirements and areas for improvement for future service deployments.
★Date and time： 10:00 – 16:00, March 4 - 6, 2004
★Location: Tokyo Tower 2F Special events hall
★Trial participants : approximately 300 people (from the general public)
★Activity：Had participants experience digital radio broadcast waves transmitted from Tokyo tower, try the service integrated with mobile telecommunication and answer a survey.
● download still image, music, video files
● experience radio shopping for event tickets / CDs etc.
● enter opinionaires to communicate requests and reactions to program
（We were unable to put MPEG-4 video on the broadcast stream so we canned the broadcast and played back on a TS playback device and inputted TS to the receiver through cable)
８． Implementation overview for
verification experiment

## Slide 10
Reactions after experiencing digital radio broadcast and mobile telecommunication integrated service
９． Results of verification experiment
162
81
92
87
93
86
93
101
110
99
47
101
80
92
93
3
12
15
3
6
1
5
4
3
2
1
4
1
1
0
7
11
14
11
14
0%
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Music download
CD sales
Opinionaire entries
Ticket sales
EPG
Fun
Somewhat fun
Normal
Not too fun
Not fun
Don’t know
No answer
I
Notes: ●音楽ＤＬは非常に評価が高い。
●ＣＤ販売は今ひとつ。⇒私個人的には、ラジオとかＴＶで見聞きして、ネットで調べて買う方なので、良いと思うが。
本問題の自由コメントとして、好意的・良い評価をしているものが多かったが、以下のようなものも、何名からかあった。（同じようなコメントが数名からあった。）
●「ラジオは“～ながら”で聞けるのが良いところなので、データ放送とか官位動画はそれに反する。」⇒「データ放送によるサービスは、後でできるような仕組みを入れたらどうか？」という意見も。
●「今回のサービスは、今ＦＭラジオと携帯電話やインターネットで実現できていることであり、真新しさはない。」⇒これについては、今回は基本的なサービスをデジタルラジオと携帯通信の連携で実現したということ。「次のアクションにつなげられるので、可能性を感じる。」「聴取者と番組の一体感が高まる」という意見があった。
●「コンテンツに期待する。」
●「ＥＰＧでエアチェック予約ができると良い」
という意見も。

## Slide 11
Networked home appliances
Home Network
Networked advanced
function /
mass storage
Car Navigation
Networked
advanced function /
mass storage
ＰＤＡ
Capable of music, video streaming, and settlement
Cellular Phone
１０．KDDI’s activities toward
broadcast/telecommunication integration
Telecommunication / broadcast integrated mobile device
Mobile phone / PDA with TV/radio reception function
Telecommunication / broadcast integrated STB
Networked Digital AV, PC, Telephones
Built-in terrestrial digital broadcast reception function
Storage / playback of broadcast wave data (server type broadcast)
Polarization of devices based on display size
Usage
configuration
Device
Ancillary
functions
Technology
Trend
Telecommunication / broadcast integrated car navigation
TV reception-capable internet navigation
Use in fixed place
Use in transport
Portable use

## Slide 12
Please visit the exhibit
Notes: ●Voice98におけるデモ放送は１７時までということを忘れていたので、どのような放送通信連携コンテンツだったかのイメージを抱いて頂けるよう、ビデオで幾つか紹介する。
●ファイル⑬：放送ダウンロード＋表示モード変更
●ファイル④：CD購入デモ
●ファイル⑪：アンケート応募