## Slide 1: myTV delivers TV Anytime
Ronald Tol
Philips Digital Systems Labs

## Slide 2: What is myTV?
2-years (~60 my) EU-funded project
1 January 2000 – 31 December 2001
Aims to provide an interoperable TV-Anytime solution for DVB and IP
Partners
  CE equipment manufacturers: Philips, Nokia
  broadcasters: BBC, RAI, NOB
  technology providers: UoL, NDS

## Slide 3: Objectives
Specify and implement a consumer platform with built-in local storage
Develop TV-Anytime services exploiting this platform
Provide true interoperability, both across different service providers and across different box manufacturers

## Slide 4: TV-Anytime functionality
“Watch what you want, when you want”
Simpler ways for the consumer to acquire TV content on local storage
  click on EPG, trailer, website
groups > programmes > segments
  series, related material
  news items, parts of programmes
Personalisation and automatic recording

## Slide 5: Combining TVA, MHP, & PVR …
Non-stored TVA
PVR
Standard MHP
Stored MHP
Standard TVA
myTV

## Slide 6: Enabled the following features …
Personalized TV channel
Trailer recording
Group recording
Remote programming
Segmentation
Downloadable applications
Browsing stored content

## Slide 7: Demonstration at IBC 2001

## Slide 8: End-to-end architecture
broadcaster
Internet
broadcast
network
myTV
box
Display
Smart
card
Internet TVA
service
provider
WAP
gateway
WAP
phone
metadata

## Slide 9: TVA data transported over DVB
Programme information
  title, synopsis, genre, technical information
Grouping information
  series, related programmes
Segmentation information
Trailer tags
Location resolution information
  channel, date, time
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: TVA data transported over DVB (cnt’d)
Resolution authority descriptor
Metadata location descriptor
PMT
Location Resolution Table
New tables in Section Format
Reference to a Manifest file in an Object Carousel
File
Manifest file
MPEG-2 DSMcc Object Carousel
File
File
File
File
File
File
File
Linkage descriptor
Trailer information Table
Trailer descriptor

## Slide 11: TVA data access over IP
Interactive search of
Programme information
  title, synopsis, genre, technical information
Grouping information
  series, related programmes
Location resolution information
  channel, date, time
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: TVA data access over IP
http://www.movies.com/resolve? CRID=crid://movies.com/12
yields XML response with resolution data
http://www.movies.com/tva.cgi? Actor=Tom+Cruise &Actor=Nicole+Kidman &Genre=thriller
yields XML response with metadata
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Nokia’s implementation
Nokia Media Terminal
Linux
MHP 1.0
Java engine
Mozilla browser
TVA module
Resident navigator

## Slide 14: Philips’ implementation
TriMedia-based STB
pSOS
MHP 1.0
Java engine
TVA module
Resident navigator

## Slide 15: BBC Navigator

## Slide 16: NOB Latest News Application

## Slide 17: What’s current? – Share it! summary
Develop an end-to-end system that enables easy access to
and transfer of personal content between local storage devices
using home-to-home (h2h) networks and that enables
innovative services through a seamless combination of on-line,
broadcast, and stored content.

## Slide 18: Contact information
Ronald Tol, Philips Digital Systems Labs
e-mail: ronald.tol@philips.com
TV-Anytime Forum, http://www.tv-anytime.org/
Gerhard Mekenkamp, Philips Research
e-mail: gerhard.mekenkamp@philips.com
http://www.extra.research.philips.com/euprojects/mytv/
John Morris, Philips Research
john.morris@philips.com
http://www.extra.research.philips.com/euprojects/share_it/

## Slide 19
For more information on Share it! contact:
John Morris, Philips Research
john.morris@philips.com
http://www.extra.research.philips.com/euprojects/share_it/