## Slide 1
Testing on Digital Terrestrial Broadcasting (ISDB-T) possibilities.
Technical overview
Source:
Tokyo Broadcasting System, Inc.
HAKUHODO,Inc.
NTT DoCoMo, Inc.
NTT DATA CORPORATION
This document is provided here as additional explanation that has been presented in last TVAF workshop as an explanatory appendix to the document AN422.
The goal of this testing is to experiment with various service scenarios in digital terrestrial broadcasting (ISDB-T). We want to achieve integrated services that merge broadcasting with portable telephones and other mobile communication terminals.
We experimented interactive broadcasting services in an environment that is very similar to actual application conditions, and thus demonstrated that the actual services can be offered.
We also examined new viewing style that used HDD video recorder, such as targeting advertisement and one-content-multi-use. The experiment used content metadata and user preferences metadata described in MPEG7. Since cellular phone is the most personal media, targeting advertisement will offer a lot of synergy effect.

## Slide 2
For HOME
Using Layer B
For Mobile
Using Layer A
H.26L / MPEG4 etc
HDTV
The system flexibility and the reliable mobile reception of Digital Terrestrial Broadcasting (ISDB-T) make terrestrial broadcasters more competent in the new wireless business world. Satellite broadcast is not good for mobile receiver. A Predominance point of digital terrestrial broadcast is that a moving receiver is easy to catch the signal.
From 2003 in Japan, we provide low profile video, sound and data services for mobile receivers by robust modulation and HDTV services for home receivers and personal video recorders by the same OFDM modulation with more carrier waves.
Narrowband
Receiver
Layer A
Layer B
6MHz
428.57KHz
HOME TV
(PVR)
The features of ISDB-T Mobile Reception and Flexibility of services
Technical overview - Transmission

## Slide 3
Personal Video Receiver
User metadata
ＨＤＤ
Segmented Ad Commercial
Video insertion
TV Set
Automatic insertion of Advertisement using consumer metadata.
TV program and ads with User Description metadata.
（Wine ad, Beer ad)
On Air
(Digital Terrestrial Broadcasting)
Beer commercial is
inserted into the ad break.
When a housewife is watching a program that is sponsored by a drink company, a wine ad is displayed. When her husband changed the setting and watches the same program, a beer ad is shown in the program ad break.
In the experiment of DEC 2001, we used content metadata and user preferences metadata that is compliant with MPEG7.
Consumer metadata and Segmentation metadata can be used to replace and insert commercial ads during a program.
Technical overview - System
User preferences metadata.
Ex.
Father’s favorite drink is Beer
Mother’s favorite drink is WIne
The present viewer
is “Father”

## Slide 4
Video
screen
Go To sponsor site
Show the sponsor site
internet
Data
screen
Data contents
+
Sponsor site URL
Push specific
video contents
Select the data content
Video content server
Request the specific
video contents
① Cooking show
③Restaurant detailed information
on the sponsor site
④A Specific restaurant
promotion video
②Restaurant guide data
BML
(Data format for digital broadcasting)
MPEG4
(AV signal for mobile)
+
C-HTML
(Data format for mobile)
MPEG4
(AV signal for mobile)
+
Convergence of ISDB-T and Mobile data service: Cooking Program Case
Mobile data Service
Digital Terrestrial
Broadcasting Service
Broadcasting
contents
（video）
Sponsored data content
server
Synchronized
Controller
Supply the sponsored
contents
We examined new contents delivery system combining digital terrestrial broadcasting service and mobile data contents delivery service.In the experiment, we used URL, not CRID. But we are convinced that it is possible to deliver contents using CRID.
Technical Overview- Data broadcasting system for Mobile Phone

## Slide 5
Test mobile receiver terminal. （By Mitsubishi Electric）
A receiver system and its battery is in the bag.
Around 2005, we expect the terminal will be the size of a cellular phone.
A liquid crystal display
Upper half: Video screen
Lower half: Data broadcasting
content screen
Screen resolution is 320×240 dots.
Data broadcasting
In this test, we provided various services to viewers, race result information services, shopping, betting,etc.
A combination of ISDB-T data broadcasting and cellular packet system is an attractive delivery method.
Test mobile receiver terminal.