## Slide 1: The Specification for Content Referencing
Alex Ashley
Editor for Content Referencing sub-group
Notes: I have been working within the TV Anytime forum for the last year, participating in the Business Models, Systems and Content Referencing groups at various times. Over the last few meetings I have concentrated on content referencing, where I am the editor for documents produced by the Content Referencing sub-group.
I work for Philips in their research lab near London, where I am currently working on a European project called “myTV” which is implementing TV Anytime functionality in a European DVB environment.
The work of the myTV project has allowed us to submit proposals to the TV Anytime forum which are based on the way we are actually going to implement a real TV Anytime system. Working on an actual implementation means that some of the difficulties inherent in such an ambitious standard as TV Anytime have been discovered. I like to think that the myTV submissions to TV Anytime reflect this depth of analysis.

## Slide 2: What is Content Referencing?
Choose product from catalogue
Get product
Take piece of paper to someone else
Pay, and get a piece of paper
Location resolution
metadata
acquire
search
select
Notes: When explaining content referencing it is useful to have an analogy to illustrate the purpose that content referencing fulfils.
I have chosen an analogy based on a shopping chain in the UK which is a mixture of mail order and conventional shopping. You choose the item you want from a catalogue (just like mail order) but you go to your local store to pick up the item.
When you get to the store you go to a till and pay for your chosen item, but rather than get the item, you get a piece of paper. You then take this piece of paper to someone else, who then goes and finds your chosen product in the stock room.
The catalogue is like the TV-Anytime metadata, the paying for the item is the selection of a content item and the piece of paper you receive is the content reference. The person going to the stock room is resolving the reference into a location.

## Slide 3: Why do we need Content Referencing?
To disconnect a piece of content from
its location in time and space
Why do we want this disconnection?
The same metadata can be used for content regardless of where and when it is broadcast
To reference groups of programmes such as an entire series
References can be given before time & channel has been decided
References work even if there is a change to the scheduled transmission time
Notes: It is an obvious question “Why do we need content referencing?” for which there are lots of answers.
My most common answer is:
“When a consumer has a hard disk based video recorder that allows them to pause live TV, they become freed from the schedules set by the broadcasters. They no longer have to arrange their time to fit with the scheduled broadcast time of their favourite shows.”
“TV Anytime wants to push this further, by allowing the user to find their favourite shows regardless of which channel they are broadcast on. From the broadcaster’s point of view, it allows the viewer to find their content amongst the hundreds of channels available.”

## Slide 4: Content Referencing Requirements
Able to reference any form of delivery medium
Able to reference an exhaustive variety of content formats
Able to reference:
  a complete content item
  a set of complete content items
Sufficient by itself to allow resolution of the location
Independent of central registration
Notes: The first step of creating the Content Referencing specification is to decide the bounds of the problem you want to solve. This slide contains some of the requirements that were given in the requirements section of the call for contributions.

## Slide 5: The CRID
CRID
CRID
CRID
An authority produces CRIDs
Each CRID contains the name of the authority
The rest of the CRID is defined by the authority
Each authority must be have globally unique name
  The TV-Anytime standard uses the DNS system
  <DNS name>/<optional path>
CRID://<authority>;<data>
Notes: Now we move on to the solution that the TV Anytime forum have chosen.
The name of the token used as a content reference is called the Content Reference IDentifier (CRID) which is a text string that can be converted by a location resolution service into either locations for the content, or more CRIDs.
The Content Referencing specification defines an organisation called the authority, which is the body that creates CRIDs that it guarantees to be unambiguous.
Each authority has a globally unique name, which is assured to be unique by using the DNS naming system.

## Slide 6: Resolving a CRID
Find out where a CRID created by an authority can be resolved
  Uses a Resolution Authority Record
  These records are pushed in the broadcast case
  IP case is not yet specified, but a DNS based solution has been proposed
Go to location given by resolution authority record
  to convert the CRID into locators or CRIDs
Notes: Once you have a CRID, at some point you need it converted into a real location, else it is not much use to you!
Resolving a CRID is a two step system. The first step is to find the place where the CRID can be resolved. The TV-Anytime Content Referencing specification uses something called a Resolution Authority Record. This record is used to map from authority name to the place where the CRIDs created by the authority can be resolved.
For example in a broadcast system, an RAR for an authority will point to the channel where location resolution information is being broadcast. In an IP based environment, the RAR will point to a server on the Internet.
Once the PDR knows where to find its location information, it can take its CRID and get it resolved into locations or more CRIDs. How this happens depends on the location of the resolving service.
For example if the resolving service is carried in a DVB transport stream, then the method of location resolution will be carried out using some DVB defined protocol.

## Slide 7: Talking to Location Resolver
The Resolution Authority Record gives location of location resolver
One or more resolution handlers will “know” how to talk to this location.
Notes: Another concept introduced in the TV-Anytime Content Referencing specification is the idea of a resolution handler.
A resolution handler is the bridge between the generic process of resolving a CRID and the protocol specific process needed to do the actual resolving.
For example a PDR might have a DVB and an IP resolution handler so that it can resolve CRIDs using either a DVB stream or a server on the Internet.

## Slide 8: An Example
C
R
I
D
“All sport by broadcaster B”
C
R
I
D
L
o
c
a
t
o
r
C
R
I
D
“Sports today” group
“Golf match on broadcaster A”
C
R
I
D
L
o
c
a
t
o
r
Golf
C
R
I
D
L
o
c
a
t
o
r
Cricket
L
o
c
a
t
o
r
L
o
c
a
t
o
r
C
R
I
D
Tennis
Notes: Here is an example of how CRIDs can be used to allow a user to find all the sports programmes for today.
The CRID for “all today’s sport” resolves into two CRIDs, on two different broadcasters. For broadcaster B, this CRID resolves into three different programmes.
The CRID for the tennis programme illustrates another feature, as it resolves into two locations because the tennis is shown once live and also repeated later that day. The tennis CRID allows the PDR to know that it can record either the live or the repeat, which may be useful if there is a schedule clash with other programmes the user wants to record.

## Slide 9: The Content Referencing Specification
The content referencing specification provides a location independent referencing tool that can be used in many ways
The TV-Anytime Systems specification will show how to use this tool to fulfil various business models
C.R. specification v1.0 allows location resolution in a broadcast environment. Future versions will allow location resolution in a bi-directional (e.g. IP) environment.
Notes: Version 1.0 of the content referencing specification was released after the 7th TV-Anytime meeting in Geneva. It provides the foundation for content referencing in all environments, and the requirements for content referencing in a broadcast environment.
It does not provide the ability to resolve CRIDs using bi-directional networks such as the Internet, as it was felt that there were insufficient contributions on this subject to produce a mature specification. A future version of the specification will provide the ability to perform location resolution in a bi-directional network environment.