## Slide 1: BBC TV-Anytime end-to-end pilot
Chris Newell
Digital Media Group
BBC R&D

## Slide 2: End-to-end pilot goals
Identify the developments required in the BBC’s internal information systems
Validate and inform the standards work within TV-Anytime and DVB
Provide test streams to PVR manufacturers for interoperability tests
Provide demonstrations to promote TV-Anytime

## Slide 3
Live combined SI / TV-Anytime database
  Group management
  Repeat management
Content Referencing service compiler (static)
Metadata service compiler (static)
Object Carousel compiler (interim transport format)
Playout system
TV-Anytime end-to-end pilot status
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: TV-Anytime end-to-end pilot head-end
Carousel
Compiler
CRI
Service
Builder
Metadata
Service
Builder
Multiplexer
Combined
SID/TVA
Database
SID: The BBC’s existing Schedule Information Database
CRI: Content Referencing Information
Existing mux
Pilot service
Update stream

## Slide 5
Linux DVB API supporting DVB-T or DVB-S NICs
Metadata service captured and cached on disk
CRI decoder supports live location resolution
Query interface provided to applications using the BBC Java TV-Anytime API (http://www.bbc.co.uk/rd/pubs/whp/whp060.html)
Applications:
  TVA plug-in for VDR (Video Disk Recorder) open source PVR
  Java-based GUI for test purposes
TV-Anytime end-to-end client status
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: TV-Anytime end-to-end pilot client
TVA
Database
CRI
Decoder
Object
Carousel
Client
TVA
Query
Manager
VDR +
plug-in
MPEG
Decoder
VDR: Video Disk Recorder (Open source PVR for Linux)
DVB
Interface
Card

## Slide 7: End-to-end pilot future development
Build Content Referencing and Metadata services incrementally to support live updates
Propagate live service updates through client to applications
Add TV-Anytime related DVB-SI (RNT etc, to support service discovery)
Support DVB Transport specification when finalised
Test against independent test streams and clients