## Slide 1: TV-Anytime on DVB broadcast networks
David White, NDS DVB-GBS Editor

## Slide 2: Overview
Draft document - GBS005r5
  “Carriage and signalling of TV-Anytime information in DVB transport streams”
  next revision available 29th July from DVB ftp site

## Slide 3: Reasons - background
Rapidly expanding PDR market
Support for PDRs in DVB is limited
Proprietary solutions mean legacy issues
Strong commercial drive for PDR support

## Slide 4: Reasons - requirements
Requirements in document PDR008
  Recording DVB services
  Acquiring associated metadata
  Referencing content for recording
  Promoting content before it is scheduled
  Robust to changes in schedule
Adopted TVA as best fit to requirements

## Slide 6: Key features
Authority linkage
  Supporting TVA resolving authority
Content Referencing Information (CRI)
  CRID resolving in a broadcast network
Metadata delivery
  Including compression, indexing and scheduled delivery
Trailer booking
  Simple, powerful and efficient
Integration with SI
  Extensions to EIT for “platform upgrades”

## Slide 7: Flexible Linkage - the resolving authority
TV-Anytime defines concept of an “authority”
  crid://<authority>/<data>
Represented by Resolution Authority Record (RAR)
How to find a RAR in a DVB network?
  Resolution Notification Table (RNT)
    fixed PID for RNTs
    lists known authorities
    references authority’s CRI
      multiple RARs per authority, DVB or internet.
    references authority’s metadata
    references other transport streams to look for RNTs

## Slide 8: Locating information on an authority

## Slide 9: Content Referencing Information - CRI sets
Different networks require different ways of organising CRI
  DTT - tight bandwidth and regional reception
    minimise cross-carriage
    distribute over transport streams
  DSAT/ DCABLE - more bandwidth, wide-area reception
    could centralise CRI on one transponder
      could carry additional, incomplete, localised set per TS
    could cross-carry all CRI
      each TS has complete CRI set

## Slide 10: Content Referencing Information - example

## Slide 11: Content Referencing Information - format
Difficult requirements
  Efficient data size
  Support prioritisation of content
  Need a route to correct result
Flexible solution
  Based on TVA indexing
  Novel, specialised index
    provides CRID compaction
    points to results (allows prioritisation)
  Efficient CRI result format

## Slide 12: Metadata delivery - flexible linkage
Based on metadata on MPEG-2 amendment
Location of linkage indicates type of data
  authority part of RNT
    content metadata (ProgramInfo, GroupInfo, etc)
  global part of RNT or NIT/BAT
    all types
    ideal for receivers caching to disk
  SDT
    instance metadata (Schedule, ServiceInfo, etc)

## Slide 13: Metadata delivery - issues under debate
Issues under debate
  Object carousel or data carousel?
  define some standard DVB indices (i.e. profile)?
  Just indexing or additional organisation of types?
  MPEG-7 BiM or something else?

## Slide 14: Trailer booking
Simple way of associating on-screen promotion with content
  Trailer for a film
  Promotion of series during credits for an episode
  Link to related material during programme
Presence of “Related material section” entry indicates a link
  Multi-language editorial text per link
    “Your chance to see walking with dinosaurs”
  Refer to content using CRID per link
  Supports multiple links

## Slide 15: Trailer booking
Watch me cooking food
Press blue
1. Record Jamie cooking
2. Record all Jamie’s programmes

## Slide 16: Trailer booking
It’s great

## Slide 17: Integration with DVB-SI events
Extending
  Extended event identification
    support for nested and overlapping events
Replacing
  TVA metadata provides much of SI functionality
  Some optional parts of SI can be done with metadata
Integrating
  Support existing platforms using EIT schedule
  Associate CRIDs with events
  Minimise impact on existing systems

## Slide 18: Accurate recording - three modes for recording
Time & date only
  Basic but an effective fall-back
Time & date + event_id
  Potentially accurate
  Supported by current systems by EIT p/f
  EIT events can’t overlap
Time & date + TVA_id
  Potentially accurate
  TVA_id events can overlap
    record ads at start and end of all events
    supports nested events
  List of TVA_ids in EIT p/f

## Slide 19: TVA_id - recording overlapping content
TV program 1
Ads
TV program 2
Ads
Ads
Record program 2
Record program 1
TVA_id 2
TVA_id 1

## Slide 20: TVA_id - recording nested content
Sports programme
Dull football
Tour de
France
Yet more football
Motorbike
race
Record all
Record
Receiver can’t tell difference between
nested and overlapping!
TVA_id 1
TVA_id 4
TVA_id 3
TVA_id 5
TVA_id 6

## Slide 21: Summary
An effective tool-kit built on TV-Anytime
  flexible linkage
  content referencing in broadcast networks
  metadata delivery
  trailer booking
  powerful event identification
  integration with SI
Some issues still to resolve
  metadata delivery
  identifying appropriate RNT
GBS0005r5 is draft specification