## Slide 1: Broadcasting Service Terrestrial Web Data Broadcasting Service synchronized with the TV Programs and Commercial Films in Japan
1st TV-Anytime Implementers Workshop
Sunnyvale,January 28, 2001
INFOCITY, Inc.
Masataka Sumikura
sumikura@infocity.co.jp

## Slide 2: Technology Concept
Web page
Broadcaster
TV screen
Content Provider
Terrestrial data broadcasts –bitcast/VBI
Terrestrial TV broadcast signal
Contents Storage Server
PC“bitcast browser ”
bitcast broadcasting system
is the “Technology & Service system” united with the Broadcasting and Telecommunication, and expanding the Internet Contents Service.
provides “Real-Time” service; Broadcasting Web data synchronized live TV program or commercial films.
also provides “On-Demand” service; Web data is sent asynchronously for TV and automatically download onto the hard disk drive of PC.
is “data-multiplexed broadcast” service; the web broadcasting service via Vertical Blanking Interval(VBI) signal for terrestrial broadcast.
These data is stored in hard disk drive of PC, and user can be accessed easily with bitcast browser at anytime.

## Slide 3: Current status of – TV stations
Tokyo Broadcasting Station (TBS) had started since July 1997.
Fuji Television (CX) had started since June 1998.
The following TV stations has started .
  MBS at Osaka, BSN at Niigata, HBC, UHB at Hokkaido, SBS at Shizuoka, CBC at Nagoya, RSK at Okayama and RCC at Hiroshima.
  Other local TV stations are planning to start .

## Slide 4: browser – User Interface
A click on the bitmark appeared on a screen displays bitcast contents.
If it is environment connectable with the Internet, it is also possible to display usual Web contents. The data can be stored and saved on the hard disk for "on-demand" access.
Click on the bitmark！
Standard Mode
（TV screen with bitmark）
Detailed mode
（TV screen and bitcast contents with bitmark）
bitmark
Browser Control
View of the bitcast contents and Internet contents
(The window to the Internet)
TV Screen
Here appears TV movie (overlay).
Bitcast Contents Chase Area
(Contents List)
The past data can also be taken out.

## Slide 5: Dynamic TV Window Mode
With bitcast technology, TV station can send original format content, called “Dynamic TV Contents” which is bundled live television picture together web data contents .
TV Window
bitcast contents
bitmark
Dynamic TV Window Mode
If bitcast browser receives Dynamic TV Contents made up of the HTML or XML content file when user is watching TV program, it shifts to Dynamic TV window mode automatically.

## Slide 6: Advanced Service by
TV dependence
Synchronized with TV or Commercial Program type
One-way
Type
Interactive
Type
Independent Type
News
Magazine
Weather forecast
On-Time Advertisement
Program added information
Closed caption
e-commerce
Audience Participation Program
Educational program
Stock quotation
Advertisement non-linked to TV Program
Television
Data Multiplex
Broadcasting
Expansion
of the new service
by bitcast
Independent and One-Way ・Distribution of clipping service
（publishing company）
・Distribution of a newspaper
（newspaper publisher）
Independent and Interactive ・Correction education
（education business）
・Offer of stock information
（Stock company）
・Introduction of new work
（Video Shop）
Synchronized w/TV and One-Way ・Sales promotion activities
（distributor） ・Profile introduction of a player
（baseball club）
Synchronized w/TV and Interactive ・Internet delivery receptionist
（home delivery Company）
・E-commerce
（Record Shop） ・Televiewer participation type quiz show
（TV station ）
Internet dependence
Service Model
Bitcast Technology takes advantage of both "popular appeal" and "interactivity" which is a strong point of ground wave telecast and Internet respectively. What kind of services does this technology offer then?
Notes: bitcastは、地上波テレビ放送の利点である“大衆性”とインターネットの利点である “双方向性”の両方を取り込んだ技術である。では、この技術によってどんなサービスが提供できるのか。

## Slide 7: Demonstration
Synchronized with Commercial and TV program.
Music Data Download Service
  User can buy Music data while watching Music TV Program.

## Slide 8: TVA Implementation
RadicalTV® software consists of following Apps.
  OS: Hard Hat Linux™ 2.0
  Analog TV tuner – Double Tuner support
  TV viewer – Trick Play support.
  HDD recording
  EPG
  Copy protection support
  Playback broadband video contents
  Mini Home Server functions
    PC is connected PDR via Home Networks.
    Watching live TV and recorded TV program.
    Remote reservation using EPG in PDR.
Next Target: PDR solution software called RadicalTV®.
Implement TVA specification target.
  Metadata and RMP(RMPI)

## Slide 9: See you Next Awaji Island Meeting.
We will give the demonstration of RadicalTV® Solution, which is implemented some TVA Spec.
If you have any question, Please send e-mail !
E-mail : sumikura@infocity.co.jp
Thanks!

## Slide 10
Bundle Model （TV turner board ・ USB Box）
NEC Corporation
I-O DATA DEVICE, INC.
Sharp Corporation
Preinstall Model PC
NEC Corporation
Hitachi, Ltd.
FUJITSU LIMITED
Annex :