## Slide 1: An Interoperable, Open Standard for PVRs
Alex Ashley
Philips Research
NAB2003 MultiMedia World Conference
“The PVR: Shifting Time and Paradigm”

## Slide 2: Introduction
Introduction to TV Anytime
The end-to-end use of TV Anytime
  Authoring metadata
  Accessing TV schedules
  Searching for interesting programs
  Enhancing content with segmentation
  Metadata aggregation
Current status of TV Anytime
TV Anytime in action
Notes: This presentation will tell you about the international standard “TV Anytime”. I will illustrate some of the features of TV Anytime by describing a TV Anytime demonstration that you can see at NAB this year.
In this talk I will describe how TV Anytime can be used to provide a complete end-to-end solution for implementing a scalable content description system.
I will also tell you what we have in our demonstration, and how it works. I hope to provide you with enough detail to understand how the system works, but without blinding everyone with too much detail!

## Slide 3
Introduction to TV Anytime
TV Anytime provides normative specifications in two areas:
Metadata - for describing content
Content Referencing - for finding content
Notes: The TV Anytime forum is an industry forum that was started in 1999 with the purpose of providing an open world standard that would allow everyone to benefit from the features enabled by a personal video recorder.
At the end of 2002, TV Anytime completed its phase one specifications.
TV Anytime has produced 4 normative specifications that cover two basic areas. One is how to describe TV content (metadata) and the other area is how to find the content that has been described (content referencing).

## Slide 4: Introduction to TV Anytime
TV Anytime metadata can describe
Programs
Groups of programs (e.g. a series)
Events (i.e. broadcast date & time)
Segments
All of these use an identifier called a CRID.
Notes: The TV Anytime specifications are able to describe a very rich set of features.I will not try to describe all of the details of TV Anytime. I will simply give you the basic introduction.
There are 4 basic things that TV Anytime metadata can describe. It can describe TV programmes, groups of TV programmes, the times and channels where these programmes can be found, and segments of programs.
All of these items of information can be linked together using an identifier called a CRID.

## Slide 5: Introduction to TV Anytime
A CRID is an identifier that can be resolved into something else
Every program is assigned a CRID. This CRID will resolve to the times and channels where the program can be found.
Every group is assigned a CRID. This CRID will resolve to CRIDs for each member of the group.
Events and segments reference program CRIDs.
Notes: TV Anytime has invented an identifier called a “content reference identifier” or CRID for short. The CRID is the identifier that glues all the other bits of TV Anytime together.
It has the feature that it can be translated (which is referred to as being resolved in the TV Anytime specifications) in to something else.
In the case of a TV programme, a CRID will resolve in to the times and channels where it can be recorded.
In the case of a group of programmes, It will resolve in to CRIDs for each member of the group.
You might be asking the question, how is a CRID assigned to a program or a group? Do I need to telephone TV Anytime HQ every time I need a new CRID?
The CRID system is based around a de-centralised naming scheme. Anyone with a registered DNS name can create CRIDs. Someone who creates CRIDs is called a CRID authority. A CRID authority is responsible for making sure the CRIDs it assigns are unique.
An example of a CRID authority might be a broadcaster assigning CRIDs to the programs it broadcasts.

## Slide 6: Introduction to TV Anytime
<GroupInformation GroupId="crid://hbc.com/foxes/all" GroupType="show" Ordered="true" NumberOfItems="2">
<BasicDescription>
<Title type="main">All episodes of Foxes ever</Title>
<Synopsis Length="short">More Foxes than you can handle</Synopsis>
</BasicDescription>
<MemberOf>crid://hbc.com/comedy/all</MemberOf>
</GroupInformation>
<ProgramInformation ProgramId="crid://hbc.com/foxes/episode1">
<BasicDescription>
<Title type="main">
The one where Fox jumps in the Potomac
</Title>
<Synopsis Length="short">
Fox goes to Washington and jumps in the Potomac
</Synopsis>
</BasicDescription>
<MemberOf>crid://hbc.com/foxes/all</MemberOf>
</ProgramInformation>
<ProgramInformation ProgramId="crid://hbc.com/foxes/episode2">
<BasicDescription>
<Title type="main">
The one where Fox drowns in the Lake of Geneva
</Title>
<Synopsis Length="short">
Fox goes to Geneva and tries to climb the fountain
</Synopsis>
</BasicDescription>
<MemberOf>crid://hbc.com/foxes/all</MemberOf>
</ProgramInformation>
CRID
CRID
CRID
Group information
Program information
Notes: They say a picture is worth a thousand words, so lets try a picture to explain how metadata and CRIDs fit together.
In the example here, we have a description of a group. This group has been assigned a CRID. If we resolve this CRID, we get the list of CRIDs for all the members of this group.
We can use these CRIDs to find out information about the individual programs that make up this group.

## Slide 7
An End to End Standard
Internet
Metadata Servers
TV Anytime
over the air
The TV Anytime stand at NAB2003 demonstrates:
authoring of metadata
a metadata aggregator using TV Anytime as its common interchange format
many different providers of metadata being used in a seamless manner by a PDR.
Metadata authoring
TV Anytime
enabled PDR
Notes: We are demonstrating that TV Anytime can provide a complete end-to-end system from creation to consumption. Along the way we show aggregation of information from many different metadata providers.
The first link in the chain is the creation of metadata. At NAB we are showing the creation of programme and segmentation metadata, using some software packages created by NDS.
The next step in the chain is a server to provide metadata to a PDR. We have metadata services from NTT, the BBC, and Tribune media services.
onTV Europe are combining all these data sources to provide one consistent aggregation.
The final step in the chain is a TV Anytime enabled PDR from Philips.

## Slide 8: Authoring Metadata
Standardised metadata allows metadata authoring tools that can be supplied to many different customers
Standardised metadata allows editing of metadata that has come from many sources
Standardised metadata allows authoring once for many destinations
Notes: One of the problems with providing consumers with lots of detailed program information is the cost of generation.
An open standard allows you to author and check the data once, and distribute to many different customers.
Using an open standard such as TV Anytime allows a whole new business to form in providing powerful easy to use tools for generating metadata. Having a standardised metadata schema gives application writers access to a much wider range of potential customers. It also removes the cost of having to provide output filters for hundreds of proprietary description schemas.
Another very useful feature of a standardised metadata schema is that it allows editing of metadata from many different sources. For example you can alter your metadata that you have received from many different sources to change from American English to British English. This job would be a lot more time consuming if each data source came in its own proprietary format.

## Slide 9: Accessing TV Schedules
Using TV Anytime data, you can create an EPG with data from many sources.
Notes: Probably the most basic feature is an electronic program guide
An EPG is useful:
  To find out what is on
  To feed a PDR’s recording “to-do” list.
  Because “VCR style” programming is far too complex!
With any new standard like TV Anytime there is a “chicken and egg” problem. Manufacturers do not want to create devices until the broadcasters are providing data, and broadcasters don’t want to provide data until there are devices that can use it.
TV Anytime’s ability to scale from a simple EPG to much more sophisticated features is one part of breaking the “chicken and egg” problem. Another import feature of TV Anytime is its ability to seamlessly integrate information from many broadcast and Internet sources.
For example, this allows a broadcaster to do a “soft” roll-out of TV Anytime by mixing broadcast and Internet delivery.
From a manufacturer’s point of view, the ability to use many metadata provides helps to reduce the risk of releasing a product that has no service to support it.

## Slide 10: Accessing TV Schedules
Schedule download is a two step process:
Find out what channels are available from the metadata service
Download listings information for selected channels for the next ‘n’ hours
service description
schedule
“What channels do you support?”
Give me channel X, Y & Z for next 24 hours
Notes: Downloading a TV schedule is a two step process. The first step is to find out what information is available. The TV Anytime specifications call this service discovery.
There are two methods of service discovery.
The one we are demonstrating at NAB is the based on downloading a service description file from a TV Anytime server on the Internet.
The other method of service discovery is over the air, using signals embedded in the broadcast. For those interested, this is based on the MPEG-2 FDAM-1metadata pointer descriptor. Alas we are not able to show this at NAB, but for those of you who were fortunate enough to visit IBC in 2001 may have seen this in action.
Note that this model assumes that schedule is stored on the box. It is also possible to use system as an on-line database and not store things locally.

## Slide 11: Searching for interesting programs
Using TV Anytime data, we can search for interesting content without knowing where or when it will be broadcast
Notes: The concept that has driven the TV Anytime standard is that consumers should be able to find what they want, when they want it.
The PVR has allowed consumers to disconnect themselves from TV schedules, and TV Anytime can make use of this feature.

## Slide 12: Searching for interesting programmes
Used to search for favorite programs / actors etc
Also uses a two step process:
Find out what fields can be queried
Make a query using supported fields.
service description
Programme metadata that matches query
“What search fields do you support?”
actor=“John Wayne” and genre=“film”
Notes: In the broadcast case, the support fields is based on what indexes are being transmitted.
When using the Internet, it is based on the service description file.
At NAB we are demonstrating searching using a server on the Internet.

## Slide 13: Segmentation of recorded material
Segmentation metadata can be used to create virtual programs from recorded material
seg1
seg2
seg4
seg5
seg6
seg7
Complete
game
seg7
Highlights
The program is recorded, and then the segmentation metadata is downloaded
The segmentation data can be used to play the “highlights” version of the program
seg1
seg3
seg3
seg4
Notes: Using TV Anytime segmentation information, a PVR can allow consumers to watch conventionally recorded material in new ways.
For example it could be used to allow a consumer to watch the highlights of a football game that has been recorded by a PVR.
As you can imagine, there are many business models that could arise from this technology, such as personalised advertising.

## Slide 14: Segmentation of recorded material
Segmentation authoring tool creates TV Anytime segmentation data
Authored data is sent to set top box
Segmentation browser allows the consumer to view the segmented program
Notes: The segmentation authoring tools allows the operator to create a virtual programme from segments of a programme.
This segmentation file can then be published to the set top box where the consumer can view the virtual programme.
An interesting extra feature of this particular demonstration is that the segmentation viewing application is an MHP application which has been downloaded to the set top box. When you have an open standard such as TV Anytime, it is not just resident software on a set top box than can make use of it. It can also be useful for application writers.

## Slide 15: Metadata aggregation
TV Anytime can also be used for business to business applications
At NAB 2003, we are demonstrating aggregation of metadata from four providers
Notes: TV Anytime was mostly designed with a business to consumer focus. It is however also useful for business to business transfers. For example in the UK, the digital television group have created a specification for how UK broadcasters can transfer their schedules using TV Anytime.
In one of our demonstrations, we show a server acting as an aggregator of metadata from many different sources.
The standardised metadata Schemas defined by TV Anytime provide an ideal common interchange format for content descriptions. As has been discovered in many different businesses, having a common interchange format allows many different systems to interoperate.
The ability for many different parties to create CRIDs is also a useful feature for metadata aggregation, as it allows them to augment the data they receive by creating new inter-relationships between pieces of content. For example an aggregator can provide cross-broadcaster links, even when broadcasters are using their own CRID namespaces.

## Slide 16: Current Status of TV Anytime
Phase 1 specifications were finished in 2002. Currently going through ETSI process
DVB GBS working on standardised method of carriage over a DVB broadcast stream
ATSC T3/S8's draft using TV Anytime metadata in its enhanced EPG standard
Several Japanese companies using TV Anytime in broadcast-mobile convergence field trials
Active liaison with Pro-MPEG Forum on MXF
P.R.O. China standardising their digital TV service. TV Anytime is being considered.
Notes:   Tokyo Pilot, Operation Crid Akasaka (NHK, TBS, NTT, Hakuhodo, Mitsubishi, Hakuhodo, Expway and Waseda University).

## Slide 17: TV Anytime in Action
At NAB2003 we are demonstrating:
the generation of TV Anytime metadata
the consumption of TV Anytime metadata
that TV Anytime is a suitable format for interchange of metadata
that TV Anytime is useful for business-to-consumer and business-to-business

## Slide 18: NAB 2003 Demonstration
The TV Anytime Forum have two demonstrations in the Pro-MPEG Forum Interoperability Center.
The Interoperability Center is in meeting room S230, which is outside the front of the Upper South Hall on the way from the Upper South Hall to the Central Hall.
The demonstration has been made possible by the efforts of the following companies: