## Slide 1: myTV: Delivers TV Anytime
IBC 2001 Demonstration
TV Anytime Implementers Workshop
Jan 2002
Notes: I have been working within the TV Anytime forum for the last year, participating in the Business Models, Systems and Content Referencing groups at various times. Over the last few meetings I have concentrated on content referencing, where I am the editor for documents produced by the Content Referencing sub-group.
I work for Philips in their research lab near London, where I am currently working on a European project called “myTV” which is implementing TV Anytime functionality in a European DVB environment.
The work of the myTV project has allowed us to submit proposals to the TV Anytime forum which are based on the way we are actually going to implement a real TV Anytime system. Working on an actual implementation means that some of the difficulties inherent in such an ambitious standard as TV Anytime have been discovered. I like to think that the myTV submissions to TV Anytime reflect this depth of analysis.

## Slide 2: The myTV Project
A collaborative research project made up of
BBC, NOB, Nokia, NDS, Philips, RAI, University of Ljubljana
Sponsored by the European Commission as part of the IST programme

## Slide 3
Overview
By combining TV Anytime, MHP and PVR functionalities, myTV has implemented a rich set of new functionalities
Non-stored TVA
PVR
Standard MHP
Stored MHP
Standard TVA
myTV
demo

## Slide 4
TV Anytime Data
Developed and implemented formats for content referencing and metadata delivery over DVB. Enables:
  trailer recording
  TV Anytime functionality for PVRs without a back channel
  time accurate recording
Developed and implemented protocols for querying TV Anytime compliant web servers.
  accesses real broadcaster schedule information from 3 different servers

## Slide 5: DVB Delivery
Descriptors in well known locations indicate where (and what sort of) TV Anytime data can be found
Content Referencing delivered in slightly compressed MPEG-2 sections
  “Root” table lists authorities resolvable with this stream
  “CRID” tables contain the actual resolution information
Metadata delivered as XML files inside a DSMCC carousel
  Manifest file maps CRID to XML file
  Updating of metadata is done by updating a file

## Slide 6: IP Delivery
Metadata and Content Referencing created from real listings information provided over the Internet by BBC, NOB and UoL
Uses a simple HTTP based protocol which is the same as the one used when submitting an HTML form
Provides CRID resolution, metadata queries and downloading of TV schedules

## Slide 7
Trailer Recording
When watching a trailer a single button click allows the advertised programme to be recorded
The user can see other information about the programme to assist their decision
Implemented by inserting a CRID into the DVB stream

## Slide 8
Remote Programming
myTV PVR
WAP gateway
Internet
Local website
3rd party website
Authenticated
HTTP
TVA?

## Slide 9
Philips myTV Platform
STB using TriMedia CPU
Ethernet card for IP connectivity
DVB-S satellite tuner
IDE hard disk
The complete system uses a TV Anytime enhanced DVB-S input stream, TV Anytime IP servers, and WAP / web clients for remote programming

## Slide 10: Nokia myTV Platform
STB using Intel Celeron CPU
Ethernet for IP connectivity
DVB-S satellite tuner
hard disk
The complete system provides the same TV Anytime features* as the Philips STB, using the SAME data.
* TVA via DVB not currently implemented

## Slide 11: Content Referencing & Metadata Servers
BBC, NOB and UoL provide TVA services
BBC and NOB use real scheduling information
UoL takes information from BBC and NOB and augments films with information from IMDB
Provides CRID resolution, metadata queries and downloading of TV schedules
Provides a simple form of metadata extensions to allow new metadata fields not defined by myTV or TVA

## Slide 12
Enhanced MHP applications
Latest news. The user can personalise the way news is presented and has DVD-like control over news items
Broadcaster navigator. A navigator designed to enhance particular content, and so offer the user greater choice

## Slide 13: Implementation Issues
TV Anytime should consider how implementations will:
Find where & what TVA data is being broadcast
Make sure updating is flexible enough for the broadcasters, but not too difficult to implement
Synchronise CRID+Metadata for adverts/trailers
Co-exist with (and extend?) interactive TV systems
Make use of the Internet (e.g. for getting TVA data, for remote programming of a PDR)